TENDER FOR THE WORK OF

RE-MODELLING & RENOVATION OF OFFICE NO 13

FOR

WESTERN INDIA REGIONAL COUNCIL (WIRC)

13, Jolly Maker Chambers No. 2,

Nariman point Mumbai-400 021.

SUB-HEAD: INTERIOR, FURNITURE, CIVIL & ELECTRICAL WORKS FOR PHASE-1

* ARCHITECTS/CONSULTANTS FOR THE WORK *

M/S BARVE CONSULTANTS

Barve House, Plot No. 177,

Sandu Marg, Chembur,

MUMBAI-400 071.

Tel. Nos.	: 2528 6084, 2528 8292, 2528 8993.

Fax							: 2528 5628

e-mail				: mail @ barveconsultants.com

suhas_barve @ iitbombay.org

###### Tender issued to M/s.____________________________________________

Tender issued by: -------------

INDEX

| Sr. No. | Particulars. | Page No. |
| --- | --- | --- |
| 1 | Instructions for Filling up of Technical Bid & Commercial Bid. | 3 |
| 2 | Preamble | 4-5 |
| 3 | Notice Inviting Tenders (N.I.T.) | 6-8 |
| 4 | Tender for the work (Contractor’s letter) | 9 |
| 5 | Special Conditions of Contract Annexure - I | 10-22 23 |
| 6 | General Conditions of Contract. | 24-27 |
| 7 | Schedule of Items. (B.O.Q.). | 28-45 |
| 8 | Summary. | 46 |
| 9 | Annexure-I (Details about Contractor). | 47 |
|  | (Annexure-I shall necessarily be filled-up by contractor). |  |

****************

INSTRUCTIONS FOR FILLING UP OF TECHNICAL BID & COMMERCIAL BID.

(Two Envelope System)

- The Tender is comprised of two parts viz. Technical Bid & Commercial Bid.

- The Tender is to be submitted in two separate envelopes marked as under:

- TECHNICAL BID (Envelope No.-1)

- COMMERCIAL BID (Envelope No.-2)

- Both the Envelopes are to be submitted at the same time and place as stipulated in the N.I.T.

- TECHNICAL BID (Envelope No.-1) shall contain following documents/Annexures duly signed and stamped on each page:

- E.M.D. in the prescribed form.

- Printed Form of Technical Bid dully filled up in detail.

- Legible Photo-copies of all relevant certificates as asked in the Technical Bid.

- Any other documents, letters, conditions, etc., that the contractor may desire to submit.

- COMMERCIAL BID (Envelope No.-2) shall contain following documents:

- Only the printed form of COMMERCIAL BID duly filled up and signed on every page is to be enclosed.

No other papers/documents/conditions/letters, etc. shall be enclosed in Envelope No.-2.

- Any tender found to be submitted in contravention of these instructions shall be rejected.

The Client/Owners/Architects reserve the right to award the work to any contractor/bidder of their choice (or to reject any bid / tender ) irrespective of the price quoted without assigning any reason.

**************

PREAMBLE

Western India Regional Council, (hereinafter referred to as “Owner/Employer”) has appointed M/s Barve Consultants, Barve House, Plot No. 177-B, Sandu Road, Chembur, Mumbai-400 071, as Consultants, (hereinafter referred to as “Consultants”) for carrying out work of Re-modeling and Renovation of Room no. 13. Jolly Maker Chambers No.2, Nariman point.

Following are the details, which describe the work, which is the subject matter of this tender and which shall be executed by the successful bidder (hereinafter referred to as “Contractor”):

- The Meeting room, Entrance lobby, etc. are to be re-furbished/renovated. Room layout may have to be changed as per drawings by demolition and /or construction of walls/partitions.

- The scope of work:

- Renovation of Meeting room, Entrance lobby.

- Tiling, Carpeting, False ceiling, Furniture making, etc.

- Electrical-wiring.

- Air-conditioning.

- Apart from these works, any other item/s of work, which may be needed, is to be carried out as directed by the consultant.

The work is to be done very selectively by trying to save (keep intact) maximum possible items which are in good condition.

1)  Due to the nature of the work, the time constraint & the space constraint, the contractor is required to have elaborate set-up of his own for factory/work-shop where the furniture could be made in full or in parts.

2) The contractor is also required to have his own Storage facility/Godown for storing Raw materials as well as Finished-goods till they are dispatched to the site.

The bidders shall give full details about such facilities in the Technical bid document.

3) The work of refurbishment/renovation of the Lecture hall, entrance lobby etc. be done by the successful bidder/contractor under this tender/contract.

4) Like wise there shall be many contractors/agencies working within the site at the same time for different works. The contractor shall extend fullest co-operation to all such agencies, and execute the items of works which may be required to be carried out for any other work/contractor/agency.

5) This Tender, chiefly covers items of Civil Works, Repairs, Interior works, Furniture, False ceiling, Carpeting, tiling, painting, etc.

6) This tender is prepared on the basis of certain items of works as mentioned above and their quantities to be executed.

*****************

NOTICE INVITING TENDERS (N. I. T.)

Sealed Tenders in the prescribed format are invited on behalf of Western India Regional Council (WIRC), of ICSI hereinafter called “Owner/Employer”, at 13, Jolly Maker Chambers No. 2 Nariman point Mumbai-400 021, for carrying out the work mentioned below, from competent contractors who are experienced in carrying out the works of similar nature and magnitude.

| 1) | NAME OF THE WORK | : | RE-MODELLING & RENOVATION OF OFFICE NO 13 for Western India Regional Council of ICSI, 13, Jolly Maker Chambers No.2, Nariman point Mumbai-400 021. SUB-HEAD: INTERIOR, FURNITURE, CIVIL & ELECTRICAL WORKS FOR PHASE-1 |
| --- | --- | --- | --- |
| 2) | NATURE OF THE WORK | : | a) Civil & Interior Works, Furniture, Tiling, Painting, etc. b) Electrical work. c) Air-conditioning. d) Any other works as directed by the Consultants. |
| 3) | ESTIMATED COST OF THE WORK | : | Rs. 18 Lakhs |
| 4) | EARNEST MONEY DEPOSIT | : | Rs. 40,000/- in form of a Pay Order/ Demand Draft in favour of “Institute of Company Secretaries of India” to be enclosed along with the Technical bid. The EMD shall be converted in to interest free Security Deposit (SD)/Performance Bond Money, in case of a successful bidder on award of work-order. In case of unsuccessful tenderers’ after award of work to successful Bidder, the EMD shall be returned without any interest or bank charges. No exemption for non submission of EMD will be given/ allowed on any account to any tenderer. The offers of bidders who have not submitted EMD will be summarily rejected. |
| 5) | RETENTION MONEY | : | Ten percent (10%) of the cost of the work done; to be recovered as Retention from the payment of every running/interim bill. |

| 6) | FINAL RETENTION MONEY | : | Fifty percent of total retention, ie. Five percent (5%) of the total cost of the work done, to be retained after the completion of the work till the expiry of the defects liability period (D. L. P.). |
| --- | --- | --- | --- |
| 7) | MINIMUM VALUE OF BILL FOR INTERIM CERTIFICATE OF PAYMENT | : | Rs. 5 Lakhs. |
| 8) | TIME PERIOD FOR HONOURING BILLS OF THE CONTRACTOR | : | Maximum Fifteen Days from the date of “Consultant’s Certificate of Payment” for the corresponding Bill of the Contractor. |
| 9) | TIME LIMIT FOR COMPLETION | : | 45 Days from the date of work order. |
| 10) | DEFECTS LIABILITY PERIOD | : | One year after the date of virtual completion of the work . |
| 11) | LAST DATE FOR SUBMISSION OF TENDERS | : | 13 th February,2012 up to 3 PM. Sealed tenders along with EMD to be submitted in the office of WIRC: 13, Jolly Maker Chambers,1st floor, Nariman point,Mumbai-400 021. |
| 12) | DATE OF OPENING OF TENDERS | : | Technical Bids to be opened on 13th February, 2012 at 5.00 PM. Commercial Bids to be opened after processing of Technical Bids on the date & time to be indicated after opening of Technical bid. |
| 13) | VALIDITY PERIOD FOR THE OFFER | : | The rates quoted in the tender shall remain valid/open for acceptance for a period of Ninety days from the last date of submission of tender. |

| 14) | COST OF BLANK TENDER DOCUMENT | : | Rs. 2500.00 to be paid in cash/DD in favour of “Institute of Company Secretaries of India” (Non refundable). |
| --- | --- | --- | --- |
| 15) | LIQUIDATED DAMAGES (LD) | : | Rupees Five thousand only per day for every day beyond the stipulated date of completion, subject to maximum of Ten percent (10%) of the total cost of work done. |

16) The powers to accept/reject any/all tenders will vest with the Owner/Employer a. And the owner / Employer do not bind themselves to accept the lowest tender and reserve the right to reject any or all of the tenders received, without assigning any reason.

## TENDER FOR THE WORK

1) I/We hereby tender for the execution of the work specified in the Notice Inviting Tender (N.I.T) which is attached hereto, within the time specified in the N.I.T., in conformity with the special conditions & General conditions as attached hereto, at the cost as quoted by me in the Bill Of Quantities (BOQ) /schedule of items attached hereto.

2) I/We have visited the site, and have read and understood the nature of the work, have understood the special & general conditions and they are acceptable to me/us.

3) Should this tender be accepted I/We hereby agree to abide by and fulfill all the terms & provisions of the special conditions of contract & general conditions of contract and in default thereof to forfeit and pay to the Owner the sums of money as decided by the consultants.

4) E. M. D. in the form as stipulated in the N. I. T, is enclosed herewith.

Name of the Contractor:

Signature of Contractor

Address:						(Before submission of tender).

Tel. Nos:   (Off.): _________________ , ___________________

(Resi.): _________________ , ___________________

Mobile: _________________________, _____________________

Dated the _________ Day of _____________ 2012.

Name of the Witness:						In witness thereof,

Address:

Occupation:							Signature of Witness to

Contractor’s Signature.

# SPECIAL CONDITIONS OF CONTRACT

- The Quality & the speed (progress/completion schedule) shall be the essence of the contract and there shall be strict adherence in respect of both the quality and the speed.

- The tenderer/bidder shall examine carefully the conditions of contract, specifications and drawings supplied herewith. He shall inspect the site and on his own responsibility, thoroughly acquaint himself with all the local conditions, materials, labour, working conditions at site etc. for the purpose of quoting the tender. All the costs, charges and expenses that may be incurred by the tenderer in connection with such examination and for the submission of tender shall borne by him and Employer accepts no liability whatsoever there of

- Bill of quantities shall be read in conjunction with the scope of work, specifications and conditions of contract, drawings given in good faith for assessment of said data by the tenderer. However, he shall make his own verification & assessment regarding the same before quoting for the work. Tenderer shall be deemed to have examined the drawings, all conditions, etc. of the contract and to have acquainted himself with the detailed description of the work to be done an the way in which it is to be carried out

- The contractor shall, when required, produce documents such as Certificate of Incorporation, Memorandum and Articles of Association in case of a Company or in case of a partnership, deed of partnership, Registration Certificate.

- The contractor shall not assign the contract or part thereof or any benefit or interest therein or there under without prior written consent of the Employer.

- The contractor shall not sub contract the whole or any of the work without prior written Consent of the Employer.

- The contract comprises of construction, Electrification, Furniture, works including all labour, material, plant, machinery, temporary and permanent works, as required for construction, Electrification, Furniture, completion, and maintenance.

- The contractor shall execute, complete and maintain strictly in accordance with the Conditions of the Contract and Specifications.

- The contractor shall provide all necessary superintendence during the execution of the work and thereafter for proper fulfilling his obligations under the contract. He will post at site a technically competent representative, as approved by the Employer.

- The contractor shall be responsible for proper setting out of the works true to the lines and levels and dimensions, as per required by the Employer. He will provide proper watching, make lighting arrangements and take care of works till they are completed.

- The contractor shall indemnify and keep indemnified at all times the Employer against all losses and claims for injuries or damage to any person or property, whatsoever, which may arise out of or in consequence of the construction and maintenance of the work.

- The Employer shall not be liable for any injury to the contractor’s workmen due to accident or otherwise. Any accident should be reported forthwith to the Employer. The contractor shall be liable to comply with all labour & other laws applicable and if any liability devolves on the employer the contractor shall undertake to indemnify the Employer.

- While transporting the materials or carrying out the works, the contractor shall not block or obstruct the traffic to the adjoining properties. He will also afford reasonable opportunities to the other contractors in the building/area for carrying out their works.

- Within eight days of the completion of the work or termination of the contract, the contractor shall clear away and remove from the site all equipment, plant, materials, debris, temporary works etc.

- The Employer and his representatives shall have the access to the works-site & work-shop etc. of the contractor all the time and the contractor shall afford all facilities for the same.

- No work shall be covered up or put out-of-view without approval of the Employer.

- Work shall be executed and measured as per relevant Standards of Bureau of Indian Standards.

- Rejected materials supplied by contractor shall be removed from the site immediately.

- Detailed description & procedure to be adopted for each item of work is given in the “Schedule of Items/B. O. Q.”, which shall be adhered to strictly.

- Makes of material to be used in all items wherever mentioned or not,

- Plywood: B.W.R marine grade, Anchor, Rock, Archid, Greenply,.

    - Teakwood framework second class CP Teak wood of approved quality, B.T.C for beading.

- Veneer: 3mm, Anchor, Timex, URO.

- Laminate: 1mm or 1.5mm as specified, Greenlam, Sundek, Newmica, Sunmica.

    - Hardware fittings: of brass or s.s. steel as specified, Magnum, Ebco, Chetna, Shalimar.

- Locks- Goodrej, Doorset Golden, or equivalent.

- Hinges concealed- Hetich, Globe, Blum, Wonder, Ebco.

- Electrical switches- Anchor , Roma, Legrand

- Wire conduits- Precision.

- Cables- C.C.I, Polycabs, Anchor.

- Wire- Polycab, Anchor or equivalent

- Tiles- Vitrified –Euro, Johnson, Kajaria.

- Plywood to be used 19mm marine BWP grade as per ISI code.

- For back 6mm B.W.P grade as per ISI code.

- Anchor, Rock, Archid, Samrat.

- Roller blind- Viesta, Armstrong or equivalent.

- Electricity (Single-phase, up to 1 HP capacity) shall be supplied free of cost to the contractor at one point. The contractor shall make his own arrangements, at his own costs, for proper distribution, taking due safety measures.

- Before quoting for the tender, contractors are expected to visit the site and study the site conditions, the nature of work and any other relevant data and shall get acquainted with it fully before quoting for the job.

- Any clarifications/additional information if required could be had from the consultants/or from the Owner.

- Every page of the tender document is to be signed by the authorized signatory. Every correction is to be clearly indicated and signed.

- The quantities mentioned in the tender documents are approximate only. And because of the nature of the work, the quantities are liable to be varied substantially or even certain items may be dropped completely. The Contractor shall not make any claims of whatsoever nature on account of variation in the estimated quantities.

- Similarly the work may demand for certain extra items to be executed. In such cases the contractor is bound to execute the extra items as per the directions of the Consultant after the rates for the extra items are mutually agreed upon. The rates for Extra-Items/ additional, altered or substituted work shall be worked out as under:

The contractor shall, within 2 days of the receipt of order to carry out the work, inform the Engineer-in-charge of the rate which he is intending to charge for such works supported by analysis of the rate or rates claimed. Rates finalized and approved by the Owner/Employer in consultation within the Engineer-in-charge on the basis of these details will be final and binding. The contractor will be paid 15% for overheads and profit on the cost of materials and labour for extra items. However, the Engineer-in-charge in consultation with the Technical Committee by notice in writing will be at liberty to cancel his order to execute such work and arrange to carry it out in such a manner as he may deem advisable, but under no circumstances shall the contractor suspend the work once ordered in writing on the plea of non-settlement of rate.

- In case of any disputes regarding quality, speed, measurements or any other matter, the decision of the Owner/Employer shall be final & binding on the contractor. If a certain decision in the matter of settlement of disputes is unaccepted by any of the parties (i.e. either the contractor or the owner) then in that case the disputed matter shall be resorted to an Arbitrator.

- The Mortar for plaster work/Concrete for any other work shall be prepared/mixed only in proper steel trays designed for this purpose.

- The debris or any other unwanted materials/ removed materials shall be removed from the premises of the Owner/Employer on day-to-day basis. And the premises of the owner shall be kept clean and clear on day-to-day basis.

- The owner reserves the right to defer or delete any of the items of work. And the contractor shall not raise any objection due to this reason.

- At a time many Contractors/Agencies shall be working in the premises (site). The contractor shall extend fullest co-operation to all other contractors/agencies.

- The Owner shall have the right at any time to amend or cancel the tender without assigning any reason whatsoever.

- Mode of Payment:

  - Mobilization advance: 10% of the Contract value will be released to you as mobilization advance for each and every discipline of works, if applicable, as per terms and conditions of the agreements of respective discipline. The mobilization advance shall be paid against your request letter along with pre approved irrevocable Bank Guarantee. The mobilization advance amount shall be deducted from your running bill at the rate of 10% of the certified amount of the bills.

  - Running Bills: Payment of running bills for the work done and approved by the WIRC for a minimum value as stipulated in the tender documents for all the disciplines of work shall be made to you within 15 days of the receipt of the said bill subject to verification by WIRC– Western India Regional Council. You will submit the running bills in triplicate along with the original measurement sheet from the Measurement Book to be maintained for each discipline separately. The Measurement Book should be numbered and shall have duplicate sheets with page numbering. The payment against your running bills should indicate cumulative quantity of work and cumulative amount for all discipline of work.

  - Final Bill: Final Value of the works done and approved by ICSI HO less security deposit as per terms and conditions of the tender document shall be released in your favour after completion and satisfactory handing over of the works to WIRC. The due amount against your final bill discipline wise shall be paid to you only after receipt of final bill along with original measurement sheets within 30 (thirty days) from the date of receipt of the final bills after deduction of advances and dues from your final bill amount.

  - Release of Security Deposit/Retention Money: The security deposit shall be released in accordance with the terms and conditions of the tender document for each and every discipline of work after the expiry of the defects liability period, subject to the conditions that you had attended to all defects noticed and communicated to you to the entire satisfaction of the WIRC during the defects liability period.

  - Recoveries: The following recoveries shall be made from all your running bills including final bill.

    - Mobilization advance @ 10% of the certified amount.

    - Deduction at the rate of 10% of the value of all the running bills for all the disciplines of works towards the Security Deposit/Retention Money. It will be released in accordance with clause (iv) above. (i.e. 50% to be retained after the virtual completion of the work till the expiry of the defects liability period [D.L.P.])

    - Income Tax Deduction, VAT, TDS as applicable.

    - Other deductions, if any.

- DATE OF COMMENCEMENT: The work will commence from the date of issue of Letter of Intent.

- PERIOD OF COMPLETION:

The time is the essence of this contract. The period of completion for the entire work of all the disciplines in each phase shall be 45 days from the date of handing over of the Site/Area inclusive of mobilization period which shall be strictly followed as per the terms and condition of tender document (s). Since the job has to be carried out in the running office, the areas shall be handed over to you as per mutually agreed completion time schedule which will be discussed with you from time to time. You will, however, submit a detailed completion bar chart indicating all the activities required for completing the job in all respects against all disciplines of work based on the agreed time schedule subject to overall completion schedule.

- SITE SUPERVISION AND MANAGEMENT:

The contractor shall submit within 2 (Two) days of signing /accepting of this work order a site Organisation Chart indicating the key person and subordinate staff to be deployed by you for each and every discipline of work. It will be very necessary for you to keep an experienced site engineer / architect of proven ability exclusively for this job during all the time of work.

- MATERIALS APPROVAL:

The samples of the material to be used will be approved by WIRC which will kept at site for inspection by WIRC at any time.

- The contractor shall provide all facilities available with you and cooperation to other contractors, if any, engaged by WIRC by affording them all facilities in the execution of their work and for properly connecting and coordinating their work with your job. You will also allow other contractor free use of your scaffolding and such other facilities already erected by you in connection with your job.

- WORK FORCE:

The contractor shall engage only experienced and capable work force, sub-contractors having good standing and experience as discussed with you.

- INSPECTION AND APPROVAL:

All works involving more than one process shall be subject to examination and approval of WIRC at each stage thereof and you will give due notice of completion of each stage. No work shall be covered or put out of view without approval of WIRC.

- TERMINATION

Subject to other provisions contained in this clause, the ICSI-WIRC may, without prejudice to his any other rights or remedy against the contractor in respect of any delay, inferior workmanship, any claims for damages and/or any other provisions of this contract or otherwise, and whether the date of completion has or has not elapsed, by notice in writing absolutely terminate the contract in any of the following cases:

| (i) | If the contractor having been given by the ICSI-WIRC a notice in writing to rectify, reconstruct or replace any defective work or that the work is being performed in an inefficient or otherwise improper or un workman like manner shall omit to comply with the requirement of such notice for a period of seven days thereafter. |
| --- | --- |
| (ii) | If the contractor has, without reasonable cause, suspended the progress of the work or has failed to proceed with the work with due diligence so that in the opinion of the ICSI-WIRC (which shall be final and binding) he will be unable to secure completion of the work by the date for completion and continues to do so after a notice in writing of seven days from the ICSI-WIRC. |
| (iii) | If the contractor fails to complete the work within the stipulated date or items of work with individual date of completion, if any stipulated, on or before such date(s) of completion and does not complete them within the period specified in a notice given in writing in that behalf by the ICSI-WIRC. |
| (iv) | If the contractor persistently neglects to carry out his obligations under the contract and / or commits default in complying with any of the terms and conditions of the contract and does not remedy it or take effective steps to remedy it within 7 days after a notice in writing is given to him in that behalf by the ICSI-WIRC. |
| (v) | If the contractor shall offer or give or agree to give to any person in WIRC service or to any other person on his behalf any gift or consideration of any kind as an inducement or reward for doing or forbearing to do or for having done or forborne to do any act in relation to the obtaining or execution of this or any other contract for ICSI-WIRC. |
| (vi) | If the contractor being a company shall pass a resolution or the court shall make an order that the company shall be wound up or if a receiver or a manager on behalf of a creditor shall be appointed or if circumstances shall arise which entitle the court or the creditor to appoint a receiver or a manager or which entitle the court to make a winding up order. |
| (vii) | If the contractor assigns, transfers, sublets (engagement of labour on a piece-work basis or of labour with materials not to be incorporated in the work, shall not be deemed to be subletting) or otherwise parts with or attempts to assign, transfer, sublet or otherwise parts with the entire works or any portion thereof without the prior written approval of the Authorized representative of ICSI-WIRC. |
|  | When the contractor has made himself liable for action under any of the cases aforesaid, the Authorized representative of ICSI-WIRC on behalf of the ICSI-WIRC shall have powers : |
| (viii) | To Terminate the contract as aforesaid (of which termination notice in writing to the contractor under the hand of the Authorized representative of ICSI-WIRC shall be conclusive evidence). Upon such termination, the Earnest Money Deposit, Security Deposit already recovered under the contract shall be liable to be forfeited and shall be absolutely at the disposal of the ICSI-WIRC. |
| (ix) | After giving notice to the contractor to measure up the work of the contractor and to take such whole, or the balance or part thereof, as shall be un-executed out of his hands and to give it to another contractor to complete the work. The contractor, whose contract is terminated as above, shall not be allowed to participate in the tendering process for the balance work. |
|  | In the event of above courses being adopted by the Authorized representative of ICSI-WIRC, the contractor shall have no claim to compensation for any loss sustained by him by reasons of his having purchased or procured any materials or entered into any engagements or made any advances on account or with a view to the execution of the work or the performance of the contract. And in case action is taken under any of the provision aforesaid, the contractor shall not be entitled to recover or be paid any sum for any work thereof or actually performed under this contract unless and until the Authorized representative of ICSI-WIRC has certified in writing the performance of such work and the value payable in respect thereof and he shall only be entitled to be paid the value so certified. |

- PLANT AND EQUIPMENT:

In order to strictly adhere to the time schedule, it will be necessary for you to arrange the best of the available equipments on this project.

- FACILITIES TO BE PROVIDED BY ICSI:

The following facilities shall be provided by the WIRC. In accordance with the following terms and conditions.

a) Water shall be made available to you at one outlet.

b) Electricity shall be made available to contractor at one outlet. Subsequent arrangement for connecting pipes/wires/tables along with all other gadgets shall be arranged by you at your cost. If may however noted that there may be occasion when water supply may not be made available and there may be power failure; in that event you will arrange the water supply and power on your own cost to maintain uninterrupted progress of work.

- FORCE MAJEURE:

This work order shall not in any way be affected nor shall any party hereto be held liable for any failure or delay in performance of any undertaking term or condition herein if such failure or delay is due to fire, floor, damage by elements, perils of the sea or air, acts of God, acts of Government, whether by law, order legislation decree, rule regulation or otherwise, resolution civil disturbance breach of the peace, declared or undeclared war, act of interference or action by civil or military authorities.

- GUARANTEE:

The entire work covered under the contract value shall be guaranteed against faulty workmanship and defective material / equipment for a period of 1 (one) year from the date of commissioning and handing over. The faulty work shall be rectified and defective material / equipment replaced at your cost and no charge to the owner within a reasonable time during the guarantee period.

- EXTRA ITEMS:

The rates for any extra item of work, if any wherever possible shall be derived from the existing rates in the Bill of Quantities; in other case shall be arrived on the basis of actual cost of material and labour plus 15% percentage of profit /overhead as stipulated in the respective tender documents for each and every discipline of work. You will, however, submit analysis of rates for each and every extra items of works as and when they arise for our approval before executing the said work.

- STORAGE:

The Contractor shall make his own arrangement for storage space for the various material required for the project at your cost. It has already been amply made clear to you that WIRC does not have sufficient storage space.

- VARIATION IN QUANTITIES:

The quantities indicated in BOQs attached to the tender document (s) may vary to the extent of 10% but the unit price thereof shall remain unaffected on this account.

- QUALITY OF WORK:

The work shall be carried out in the highest standard of workmanship and according to the drawings / specification / colour chart. Sample of all components will be approved by WIRC. Any work not approved by WIRC shall b rectified or removed and replaced to entire satisfaction at your cost.

- LIQUIDATED DAMAGES:

The liquidated damages at the rate as specified in the tender document (s) for each and every discipline of work shall become leviable in the event of delay in completing the job. The liquidated damages shall be levied as under:

- For deficient work as per the miles stones indicated in the tender documents:

Liquidated damages proportionate to the deficient work subject to 10% if the value of the contract.

- Failure to complete the entire work within the completion time schedule.

Liquidated damages @ Rs. 5,000.00 per day subject to maximum of the 10% of the contract price.

- DISCREPANCIES:

All discrepancies in drawings and specifications or anywhere in the Project Work should be brought to the notice of WIRC immediately on notice and / or on its occurrence.

- DEFECTS LIABILITY PERIOD:

The defect liability period of 12 months shall be counted from the date of handing over the complete work.

- DETAILS OF CONTRACT TO BE KEPT CONFIDENTIAL:

You shall not exhibit or permit to be exhibited any advertisement on the works or shall not publish disclose the details of the contract in any trade or technical paper or elsewhere without prior permission from WIRC.

- FACILITIES TO BE MAINTAINED IN THE WORKING OF WIRC OFFICE:

All areas, passages, drive ways, stair cases which have not been handed over for project work shall be kept neat and clean all the time; some barriers shall be made by you to bifurcate the working area and non-working area, and maintaining all the services like water, electricity, sewer/waste water disposal without any disruption of services shall be made by you without any extra cost.

- OTHER LEGISLATIONS:

The contractor shall comply with the various labour legislations and safety regulations and safety codes presently in force during the pendency of the contract Proper care to be taken by the labour while working in the premises of WIRC and if any problem arises out of the work / during the work it is the liability of the contractor to take care of their welfare and in no way WIRC is liable. It is the whole and sole responsibility of the Contractor for his labour or any person employed by him if meets with any accident, electrical shock, fire, snake bite etc. etc. The contractor should also take the insurance for his people working in WIRC. And if any liability devolves on the employer The contractor shall undertake to indemnify the Employer.

- PERFORMANCE BOND:

The tenderer, whose tender is accepted by the owner is required to provide Performance Bond for the due and faithful performance of the contract for an amount equivalent to 2.5% (two and half percent) of the contract amount or by an irrevocable Bank Guarantee of an equivalent amount in the format approved by the WIRC from any nationalized Bank in favour of the Institute Of Company Secretaries Of India. The Bank Guarantee so submitted shall be valid for six months more than the stipulated/extended date of completion. The performance bond money/Bank Guarantee shall be submitted within 10 days of the award of work or at the time of signing of the agreement whichever happens earlier. Else the Ernest Money Deposit (EMD) of deposited with the Tender shall be retained and treated as Performance Bond Money.

- DISPUTES:

a) ARBITRATION

If any dispute arise about the interpretation of the terms of the agreement or in relation to this agreement the same shall be referred to the Sole Arbitration of the Secretary & CEO, The WIRC, or his nominee. The arbitration shall be held in accordance with the Arbitration and Conciliation Act, 1996 and the decision of the Arbitrator shall be final and binding on the parties.

b) Jurisdiction

All disputes arising out of this contract are subject to the jurisdiction of Courts in Thane/Mumbai.

- This letter together with correspondences, tender specifications, bill of quantities formal agreement when executed including special conditions and technical conditions of the tender document shall constitute a binding contract between the parties.

- Any matters/conditions which deviate from the Tender Specification (s) and Bill of Quantities shall not be accepted and shall not be binding unless it has been specifically accepted by the WIRC in writing.

- The contractor shall abide by the rules & regulations as set forth by the “Society” & Competent Authorities these shall supercede any other conditions stipulated in the tender. A copy of Rules & Regulations set forth by the Society are annexed herewith as Annexure-I.

***************

ANEXURE-I

Rules & Regulations set forth by the Back bay Premises Co-op Society Ltd.

Following precautions to be taken while refurbishment of premises.

- Tampering with beams columns & chajjas, Rcc pardis, uprooting of floor tiles is not allowed.

- Removing existing walls & constructing new ones is not allowed.

- Tampering with waterproofing of toilet blocks is not allowed.

- The common areas shall not be encroached upon.

- The construction material shall be taken only by the staircase & the same shall be kept clean.

- No load shall be borne by the chajjas.

- No worker shall stay in office premises after 11.00 p.m.

- The in-charge of renovation work will report to duty supervisor before commencing & closing of the work.

- Fire preventive measures should be observed by the workers. No smoking/ cooking is permitted on site.

- The debris material shall be brought to the ground floor only either on Saturday after 6.00 p.m. or Sunday in morning. And the same shall be shifted out on Sunday evening.

- The contractor shall furnish the list of staff along with photographs engaged for various works & also ensure discipline at worksite. They should wear badges indicating their names as well as photographs, duly signed by contractors representative & security officer.

- The contractors representative shall be present at all time on site.

- Timings for work:

a) No renovation shall be carried out during working hours( Monday to Friday) 8.30a.m. to 6.30 p.m. & Saturday 8.30 p.m.to 2.00 p.m.

b) Renovation work is permitted between 6.30 p.m to 11 p.m.( Monday to Friday)

c) Renovation work is permitted between 8.00 a.m. to 11.00 p.m (Sunday)

d) Renovation work is permitted between 2.30 a.m. to 11.00 p.m (Saturday)

GENERAL CONDITIONS OF CONTRACT

- The rates quoted shall be written both in words and figures very clearly. Any corrections/over-writings shall be signed. Every page of the tender document shall be signed by the authorized signatory.

- Every page of the tender document is serially numbered with a mention of total number of pages. Contractors shall check the same carefully and shall inform the Consultants if any page is found missing, or in duplicate, etc. Especially any problems with page numbers of Bill Of Quantities (B. O. Q.) shall be brought to the notice of the consultants immediately, before submission of Tender.

- Every item in the Tender is given a distinct “serial number”, which is mentioned in the column “Sr. No.” in B.O.Q. (schedule of items). Contractors shall ensure that items are numbered serially starting from number One, without any missing serial number. The “Tender Item Number” as appearing in the “Brief Description of the Items” in B.O.Q. are only for our office reference, and do not have any relevance. The “Tender Item Numbers” would not be in serial order.

- In case the contractor is not the proprietor of the firm, then the tender shall be signed by the authorized signatory/power of attorney and copy of the legal instrument shall be enclosed along with the tender.

- The rates quoted shall include all the costs like costs of materials, labour, contractor’s profit, costs of scaffoldings, rents, fuels, cost for curing, cleaning, disposing off debris/unwanted materials. The rates shall also include all the taxes/levies/cess, etc., such as octroi, or any other taxes that may be applicable/ or may become applicable, (except for VAT & Service Tax), and the contractor shall not claim anything extra on account of any such taxes. T.D.S. shall be deducted as applicable.

- Only VAT & Service tax shall be paid extra (separately) as applicable, such of these applicable taxes, as prevailing on the date of submission of tender, shall be specified, wherever applicable.

- The rates shall also includes all the costs for proper & adequate temporary support systems, proper & adequate protection/covering arrangements for effective protection of un-removed furniture/fixtures/floorings/walls/door/windows/lifts etc. and other materials/goods while working within the occupied premises of the houses/flats/offices etc.

- The rates shall also include the necessary costs towards testing of materials as per directions of the consultants.

- The rates quoted shall be firm and binding during the entire currency of the work. And Escalation &/or Price-Variation shall not be paid on whatsoever account.

- The contractor shall arrange all the materials, labourers, tools, tackles, etc., required for the work. The Owners shall not supply any material.

- The safety of workmen shall be the sole responsibility of the contractor. In the event of any accident the contractor is liable for payment of compensation as per provision of the law. The contractor shall insure his workmen under the Workmen’s Compensation Policy and submit the Xerox copy of the policy to the consultants prior to commencement of the work.

- The contractor shall take sufficient precautions like providing safety belts, helmets, etc, to the workmen so as to achieve real safe working conditions so that accidents shall be avoided.

The owner shall not be held responsible for any laps on the part of the contractor.

- The contractor shall also keep himself & the Owner insured & indemnified against any “third party claims” including any claims due to damages to property or vehicles parked within the premises of the owner.

Thus the contractor shall keep the owner indemnified against any such claims.

- The contractor shall take all the necessary precautions so as to cause minimum disturbance/nuisance. Also the contractor shall take all the necessary precautions to prevent any damages to the property of the owner /occupants of the building, during the execution of the work.

- The contractor shall commence the work within two days from the issue of the work order or from the date of Agreement, whichever is earlier. In case of failure to do so, his E.M.D. shall be forfeited and the owner shall be free to award the work to any other agency.

- The contractor shall maintain proper speed and quality during the entire currency of the work. At any stage if it is found that the contractor is not in a position to cope up with the requisite standards of speed and quality, then under such circumstances, the owner reserves the right to get the work done, at the risk & costs of the contractor, from any other agency as deemed fit. The decision of the consultants in this regard shall be final and binding.

- The contractor shall give guarantee in the prescribed format for five years for the work items executed by him. And he shall at once rectify any defects that may be noticed during the period of the guarantee at his own costs.

- The mode of measurements shall be as indicated under the relevant item in the Bill Of Quantities (BOQ)/ Schedule of work (wherever so indicated), otherwise it shall be as per the norms of I.S.I.

- The contractor, at his own cost, shall replace the broken glasses/windowpanes/sliding windows and shall make good any damages that may occur during execution of the work.

- The procurement storage & safety of materials, shall be the responsibility of the contractor alone.

- Advance payment shall be released on account of procurement of material on site, at the sole discretion of the owner.

- The contractor shall appoint a competent supervisor who will remain on site for day-to-day supervision and to receive the instructions from the consultants and the owner.

- A triplicate book shall be maintained on site as a “Site Order Book” and any instructions written in the book by the consultants/representative of the owner shall be equivalent to a notice properly served on the contractor and received by the contractor.

- On award of the work, the contractor shall submit a detailed Time schedule of work and shall get it approved from the consultants.

- It shall be the sole responsibility of the contractor to obtain the necessary permissions/approvals/clearances from the local Bodies/Municipal Corporation etc. at no extra cost. The contractor shall not violate any laws/rules/statutory requirements prevailing during the period of contract. The rates as quoted by the contractor shall deem to include all the costs for all such permissions/approvals/etc.

- Any mandatory deductions such as T.D.S. (Income Tax), VAT, etc, which may be required to be deducted from payments made to contractors shall be deducted appropriately as per the prevailing rules/laws.

- If due to any reason the work is suspended mid way; or the contract is terminated by the Owner, then in such event contractor shall not claim anything extra as compensation. Only the actual items of work executed till the date of suspension, on the basis of accepted rates shall be measured and paid to the contractor.

- In case of any dispute between the Contractor & the WIRC, then in that case the disputed matter shall be referred to an Arbitrator to be appointed by The Secretary & CEO, The WIRC. The arbitration will be conducted in accordance with the Arbitration & Reconciliation Act, 1996 and the decision of the Arbitrator shall be binding on the parties. The arbitration proceedings will be conducted in Mumbai.

*****************

#### TENDER FOR THE WORK OF

#### RE-MODELLING & RENOVATION OF WIRC ROOM NO. 13

#### For

WESTERN INDIA REGIONAL COUNCIL

13, Jolly Makers Chambers,1st floor, Nariman point MUMBAI 400021.

SUB-HEAD: INTERIOR, FURNITURE, CIVIL & ELECTRICAL WORKS FOR PHASE-1

Bill Of Quantity (B. O. Q.)/Schedule of Items

| Sr. No. | Tender Item No. & Brief Description of Item | Estimated Qty. | Unit | Rate | Amount in Rs. |
| --- | --- | --- | --- | --- | --- |
| 1 | REMOVING PARTITIONS: Dismantling carefully the partitions of any type, in office & disposing of the same & carting away the same. | 55 | Sqmt |  |  |
| 2 | REMOVING FALSE CEILING IN PARTS (SELECTIVELY): Dismantling carefully the existing false ceiling wherever required & as directed (in Parts) & disposing of same. & carting away the same. | 120 | Sqmt |  |  |
| 3 | REMOVING STORAGE UNITS & TABLES: Dismantling carefully un-wanted storage units & office tables & disposing of same. |  | L.S. |  |  |
| 4 | REMOVING DOORS: Dismantling carefully the doors in office & disposing of same & taking away. | 7 | Nos. |  |  |

| 5 | REMOVING ELECTRICAL CABLES & FIXTURES: Dismantling the all Electric wires, fittings, fixtures etc. complete as directed. |  | L.S. |  |  |
| --- | --- | --- | --- | --- | --- |
| 6 | FALSE CEILING (GYPSUM): Providing and fixing false ceiling of precast gypsum board of 12mm thick over framing of MS roll formed with G. I. channels, with all required paper tape, jointing compound, finishing with application of top coat as per manufacture’s specifications, (Gypsum India or Coral) All G.I. steel sections shall be rolled formed of B.Y.P steel. | 120 | Sqmt |  |  |
| 7 | PANELLING WITH (VENEER): Providing and fixing acoustic panelling on walls in lecture hall with T.W. frame of 2’x 2’ C/C (or framework of aluminium sections of 2”x2” & 1.5 thk at 2’ c-c), on walls, 12 mm ply of BWP with holes of 4 mm, some portions with double layer Ply. P/F 3 mm veneer of approved design finish complete. (Basic price for veneer -180 Rs / sft.) | 55 | Sqmt |  |  |
| 8 | PANELLING WITH (DECORATIVE VENEER):Providing and fixing acoustic panelling on walls in lecture hall with T.W. frame of 2’x 2’ C/C, (or framework of aluminium sections of 2”x2” & 1.5 thk at 2’ c-c), on walls, 12 mm ply of BWP with holes of 4 mm, some portions with double layer Ply, P/F 3 mm veneer of approved design finish complete. | 10 | Sqmt |  |  |
| 9 | PANELLING WITH CARPET: Providing and fixing acoustic panelling on walls in lecture hall with T.W. frame of 2’x 2’ C/C, (or framework of aluminium sections of 2”x2” & 1.5 thk at 2’ c-c), on walls, 12 mm ply of BWP with holes of 4 mm, some portions with double layer Ply, with Teak Wood moulding, P/F carpet approved design finish complete. | 9 | Sqmt |  |  |
| 10 | INSULATION: P/F 75 mm thk. 32 kg/m3 density fibre rock wool insulation (without foil wrapped in polythene cover) & fixing jali on both sides including cost of all materials making to the require size, scaffolding wastages all as per the specifications and as directed by Architect. | 81 | Sqmt |  |  |
| 11 | ACCOUSTIC PANEL IN Meeting room: P/F framework of T.W. 50mm x 37.5mm treated wood, fixing glass-wool with mesh and fixing Acoustic panel of 9mm thk, sound absorption more than 0.65, density 237kg/m3, humidity resistant, the colour & texture of tile shall be as directed by the Architect/Consultant, germs proof with 10 years warranty complete, etc. | 10 | Sqmt |  |  |
| 12 | PARTITION: P/f Partition with framework of 2"x3" T.W. frame (or framework of aluminium sections of 2”x2” & 1.5 thk at 2’ c-c), & fixing 12mm ply on both sides ( waterproof ply 710 grade) & fixing veneer on one side (P u coating) & combination of carpet & veneer on other side complete etc ( Basic price for veneer : 180 Rs /sft. | 29 | Sqmt |  |  |
| 13 | DOOR: P/f 75mm thk door with inserting rockwool & veneer on both sides with vision glass as directed on by consultants. | 2 | Nos |  |  |
| 14 | PLATFORM: P/F 9” to 12” raised platform constructed with frame of size 3”x2” thk teak wood and 19mm BWP plywood on top, complete as per drawing .(Top of the Platform to be finished by approved surfacing, which shall be paid separately under relevant item). | 12 | Sqmt |  |  |
| 15 | WOODEN FLOORING (Top layer surfacing): P/F Wooden flooring in BTC wood, having thickness 10 mm, on the prepared surface. | 12 | Sqmt |  |  |
| 16 | CABINET FOR SERVER UNIT: P/F Cabinet in Marine ply with approved laminate inside & outside & louvered shutters with necessary hardware fitting. | Q.R.O |  |  |  |
| 17 | REFURBISHMENT OF EXISTING TABLES: P/F veneer of approved design, of approved brand, 1 MM thick on old surfaces with fixing on 6mm BWP ply with adhesive complete, beading complete. | 16 | sqmt |  |  |
| 18 | POLISH (On old Surfaces): P/A French Polish to match the existing polish complete etc. | 61 | Sqmt |  |  |
| 19 | POLYURETHANE COATING: (On Old Surfaces): Scratching & p/a 3 coats of P.U. coating of approved shade, on old surfaces/furniture, as directed by the consultants, complete. | 24 | Sqmt |  |  |
| 20 | LAMINATE FIXING: P/F laminate of approved design, of approved brand, 1 MM thick on old surfaces with fixing on 6mm BWP ply with adhesive complete, beading complete. | Q.R.O | Sqmt |  |  |
| 21 | TACK BOARD/ PINUP BOARD: Providing and Fixing tack boards/ pin up board on 12mm plywood and T. Wood frame-work covered with cotton fabric of approved make and colour complete etc. | 6 | Sqmt |  |  |
| 22 | PODIUM: Refurbishing of podium with veneer & pu coating. | 1 | Nos |  |  |
| 23 | SOFA: Supplying of sofas in 2 seater units as per design of m.s. tubular construction with cushioning of 102mm high density P.U. foam seats and 76mm foam finished in fabric of approved make and colour. Upholstery Rs. 350/- per mt | 2 | Nos |  |  |
| 24 | P/F CARPET (FOR FLOORING & ON WALLS/PANELING): P/F synthetic carpet, on the floor OR walls/Paneling, of type 100% BCF Polypropylene (Bulk Continuous Filament), with 6mm poly under layer having following specifications: Machine Gauge: 2.54 mm (1/10”), 39.4 rows/100 mm. Stitch Rate :45/10 cms Construction :Plain Loop Density Factor: 177,300 tufts/m2 Tufted Pile Weight: 650 gms/m2 Tufted Pile Height: 5 mm (+/-5%) Primary Backing: 90 gms/m2 Secondary Backing: 55 gms/m2 Moth Proofing: Naturally Resistant. Bond Strength: 30 Newton. Tuft Withdrawal Strength: 20 Newton Flammability: Passes the test Static Generation: Under 3KV. The carpet shall be fixed with approved adhesive like Fevicol-SR 505. | 26 | Sqmt |  |  |
| 25 | RENOVATION OF MAIN DOOR USING VENEER: As per architects drg. With approved Veneers & PU coating & approved Handles & hardware, as per architect design. | 1 | Nos |  |  |
| 26 | RENOVATION OF MAIN DOOR USING LAMINATES: As per architects drg. With approved laminates & approved Handles & hardware, as per architect design. | QRO | Nos |  |  |
| 27 | CERAMIC TILES FOR FLOORING: Providing and laying approved ceramic tiles on existing ones flaming with gas & laying tiles with tile-o-tile cement of approved Brand, any colour, size, as approved by The Consultants/ Owners, for flooring, in required position, filling joints with white/colour cement slurry, and cleaning complete; as directed by The Consultants. | 9 | Sqmt |  |  |
| 28 | CERAMIC TILES FOR DADO: Providing and laying approved ceramic tiles on existing ones flaming with gas & laying tiles with tile-o-tile cement of approved Brand, any colour, size, as approved by The Consultants/ Owners, for flooring, in required position, filling joints with white/colour cement slurry, and cleaning complete; as directed by The Consultants. | 51 | Sqmt |  |  |
| 29 | METAL FALSE CEILING: P/f metal false ceiling in toilet. | 10 | Sqmt |  |  |
| 30 | E.W.C. in Light colour: Supplying, fitting and fixing in position white glazed earthenware wash down, European type, W.C. of approved make, (Cascade series of Parry ware make or other approved equivalent) conforming to IS:2556 Part-II with ‘P’ or ‘S’ trap, with or without vent hole, including matching coloured, ’solid plastic’ seat and cover of ‘Commander’ brand, 10 liter capacity vitreous low level syphonic type flushing cistern of approved make, (Parry ware make or other approved equivalent) together with necessary C.P. brass fittings, supporting brackets, C.P. brass flush bend with C.P. brass couplings 15 mm dia, overflow pipe with mosquito-proof cover, C.P. brass Angle cock, PVC connectors, C.P. bib cock, etc. all the fittings complete, including cutting through walls and floors and making good all damages, all material and labour complete; as directed by The Consultants. All the fittings & fixtures shall be got approved from the consultants prior to fixing in position. | 2 | Nos |  |  |
| 31 | WASHBASIN: Light Coloured: Supplying, fitting and fixing in position white or coloured glazed vitreous China wash basins of the following types and sizes with central tap hole including C.I. brackets painted with one coat of red oxide zinc chromate primer and two coats of approved synthetic enamel paint, 15 mm dia chromium plated brass Jaguar make approved deluxe pillar tap, inlet connections with all fittings like C.P. angle cock, PVC/C.P. connectors, 32 mm dia C.P. brass waste coupling, bottle trap & fittings, chain and rubber plug, etc. complete, all materials, tools and labour complete; as directed by The Consultants. All the fittings & fixtures shall be got approved from the consultants prior to fixing in position. a) 600 mm ´ 450 mm size, Light coloured, of Hindustan, or Parry ware Cascade series or other approved equivalent make. b)450 mm ´ 300 mm, Light coloured, of Hindustan, or Parry ware Cascade series or other approved equivalent make. | 2 | Nos |  |  |
| 32 | P/F HEALTH FAUCETS/HANDSPRAY UNITS: P/F Health Faucets/Hand-spray units for WC, of Jaguar make, CP, including all bends, couplings, flanges etc., complete as directed. | 2 | Nos |  |  |
| 33 | P/F TWO BIB COCK: P/F Two-way Bib cock for Health Faucets, CP, Jaguar make, as directed, including all the accessories & fittings, complete. | 4 | Nos |  |  |
| 34 | P/F PILLAR COCKS: P/F C.P. Brass Pillar cocks, heavy duty, Jaguar Make, as approved by the consultants, including necessary fittings, etc., complete, as directed. | 2 | Nos |  |  |
| 35 | P/F ANGLE STOPS: P/F C.P. Brass Angle stop cock of Jaguar make with all fittings, etc., complete as directed by the consultants. | 4 | Nos |  |  |
| 36 | HALF STALL URINALS: P/F & installing glazed chinaware (CERAMIC) half stall urinal of approved make, with all the necessary fittings & fixtures, inlet & outlet connections, etc. complete; as directed by The Consultants. | 2 | Nos |  |  |
| 37 | URINAL PARTITION (GRANITE): Both sides Polished: Supplying, fitting and fixing in position urinal partitions of approved Granite stone of any colour, of required size as per the design, 25 mm thick, with edges and corners shaped in round securely, with edge-moulding, fixed in wall including cutting chases, grouting the same with PCC (1:1 1/2:3) and polishing the partition from all sides; as directed by The Consultants, all materials, tools and labour complete; as directed by The Consultants. | Q.R.O |  |  |  |
| 38 | Urinal partition ( laminated hard board): P/f 12 mm thk laminated hardener sheet as partition | 2 | Nos. |  |  |
| 39 | P/F MIRROR: Providing & fixing mirror in toilet on 4nos. Brushed ss spacers as per design. | 2 | Nos |  |  |
| 40 | SOAP CONTAINER :Providing and fixing in position approved type C.P. liquid soap container with holder of approved design including C.P. brass screws, cutting holes in walls, rawl plugs etc. all materials, tools and labour complete; as directed by The Consultants | 2 | Nos |  |  |
| 41 | TOWEL RAIL: Providing and fixing in position approved C.P. towel rail 25 mm dia and 600 mm long with C.P. brackets including making holes in walls, rawl plugs, C.P. brass screws etc. as specified all materials, tools and labour complete; as directed by The Consultants. | 2 | Nos |  |  |
| 42 | FIBER DOOR FOR TOILETS: P/F polythene Fiber door/ moulded doors for Toilets | 4 | Nos |  |  |
| 43 | Door Frames for Toilet: (WOODEN TEAK WOOD FRAMES) Providing & Fixing C. P. Teak Wood frames for doors of size 150 mm x 75 mm, complete with rebates, chamfers, rounding edges, etc., painted with approved wood primer, with inaccessible parts painted with approved wood preservative & black Japan, necessary hold fasts, screws, nails, keys, wedges etc., as specified; all materials and labour complete; as directed by The Consultants. | Q.R.O. | Cum. |  |  |
| 44 | DOOR FRAMES FOR TOILET: (Granite):: P/F Granite patties in step form as directed, to form a frame for windows, doors etc. Total width of both the patties shall be around 300 mm (Basic rate of granite: Rs. 2000/- per Sqmt.) | 23 | Rmt |  |  |
| 45 | LUSTRE PAINT: Providing & Applying three coats of Luster paint of approved make and shade, over a coat of approved primer, as specified, on any surfaces, at all heights, including scaffolding, all materials, tools, plant and labour complete; as directed by The Consultants. (total 4 coats including primer) | 220 | Sqmt |  |  |
| 46 | REMIUM ACRYLIC EMULSION: (for Interior) Providing & Applying three coats of Acrylic Emulsion paint of approved make and shade/s, over a coat of approved primer, after necessary surface preparation, putty-filling, as specified, on any surface, at all heights, including scaffolding, all materials, tools, plant and labour, etc., complete; as directed by The Consultants. (total four coats including primer). | Q.R.O. | Sqmt |  |  |
| 47 | P. O. P. FINISH: Providing plaster of paris punning on plastered surfaces including removing of neeru finish if required, scaffolding, curing, etc., all materials, tools, plant and labour, complete; as directed by The Consultants. | Q.R.O | Sqmt |  |  |
| 48 | VITRIFIED TILES FLOOR: Providing and laying approved vitrified tiles of any Brand in patches ( wherever damaged), any colour, any size, as approved by The Consultants/Owners, for flooring in required position, laid on a bed of 1:4 cement mortar including neat cement float, filling joints with white/colour cement slurry, curing and cleaning complete; as directed by The Consultants. (Basic rate of Tiles: Rs. 1000/- per Sqmt.) | 35 | Sqmt |  |  |
| 49 | WALL PAPER: P/F wall-paper of approved brand of Shade, Texture, having Wt of 230 to 320 GSM, embossed/ plain, in any position like on the wall, ceiling, etc., complete with approved glue, complete as per the directions of the Consultants. (Basic Rate of Wall paper: Rs. 1200/Sqmt). | 17 | Sqmt |  |  |
| 50 | ANTI TERMITE TREATMENT: Providing Pest Control & Anti-termite treatment by appointing a specialized agency as per the specifications mentioned by the Bureau of Indian Standard & Agencies specification ( Whichever is higher) for General Civil , Plumbing / Drainage & timber / Carpentry works , Gypsum related work including 5 Years guarantee under suitable undertaking on stamp paper etc complete as directed . (Mode of Measurement to be on lump sum basis for the entire office block.) |  | L.S. |  |  |
| 51 | CLOTH: P/fixing cloth for panelling | Q.R.O | Sqmt |  |  |
| 52 | DOOR CLOSERS: P/F Door closers of approved brand, heavy duty, ISI mark, as directed | 3 | Nos. |  |  |
| 53 | POP PROTECTION: P/A POP on floor tiles etc, for protection of tiles, removing the same after the work is completed. | 100 | Sqmt |  |  |
| 54 | ROLLER BLINDS: Providing and fixing Roller blinds for windows of approved make and colour. | 10 | Sqmt |  |  |

-------------------------

TOTAL of PART A: Rs.															-------------------------

PART-B: ELECTRICAL-WORKS

| 1 | ELECTRICAL POINT WIRING: Providing and fixing point wiring, concealed in pipes within walls, open in casing-capping on RCC ceiling & beams etc., with precision brand pipe and Modi brand casing-capping with 3 nos. of 1.5 sqmm flexible bright annealed multi strand bare copper conductor for voltage grade upto 1100V, The wires all accessories, screws and washers, with Anchor make Piano type switch, socket etc. with its cover plate of 3mm, Hylam sheet, switch board and out let boxes of 18 SWG red oxide painted or P.V.C box; complete with accessories, angle holders, baton holders and ceiling roses, etc. complete, in all respects, to the satisfaction of the consultants: 5 Amp switch controlling one light or fan point Length up to 10 RMT Length up to 20 RMT 5 Amp Socket outlets 3 pin, with 5 Amp S. P. switch (On common board, half point) 5 Amp Socket out let, 3 pin, with 5 Amp, S. P. switch as an independent point. 5 Amp 2 way controlling switch for one point: Length up to 10 Rmt. Length up to 20 Rmt. | 25 20 15 7 5 Q.R.O | Nos Nos Nos. Nos. Nos. |  |  |
| --- | --- | --- | --- | --- | --- |
| 2 | 15 AMP SOCKET: Providing and fixing 15 Amp. Switch socket Anchor, Roma make or equivalent modular switch plate & concealed box. | 10 | Nos. |  |  |
| 3 | CIRCUIT WIRING: Providing and fixing circuit wiring, concealed in pipes within walls, open in casing-capping on RCC ceiling & beams etc., with precision brand pipe and Modi brand casing-capping with 3 nos. wire system, wire lug at all wiring end and numbering the wire to the satisfaction of consultant (From D.B to Individual 15 amp socket, class room & lighting board) 2.5 Sqmm: 2Nos, & 1.5 Sqmm (Earthing): 1 No wires 4 Sqmm: 2Nos & 2.5 Sqmm: 1 No wires 6 Sqmm: 2Nos & 4 Sqmm: 1 No wires. | 50 50 50 | Rmt Rmt Rmt |  |  |

| 4 | Supplying and installing Cat-VI annealed copper conductor PVC insulated and PVC sheathed 4 pair cables for Data with twisted pair colour coded in rigid PVC conduits clamped on walls/ceiling. | 70 | Rmt |  |  |
| --- | --- | --- | --- | --- | --- |
| 5 | Supplying and Installing of 25mm conduits for Access control/camera cables. | Q.R.O. | Rmt |  |  |
| 6 | Providing and fixing RJ 45 for Computers (D’link make). | 5 | Nos |  |  |
| 7 | Supply and Installation of 4 core 6 sq mm PVC armoured copper conductor cables with 2 Nos 12 SWG copper earth wire for lighting/power and AC wiring including cable end termination glands. | 15 | Rmt |  |  |
| 8 | SITC of 2x36 watt F P –L ( H F) with p5 paralite louver & electronic ballast with 3 Nos. of 36 watt lamp similar to Havells cat No. LHCC 22236127 or equivalent make. | 8 | Nos |  |  |
| 9 | S.I.T.C. of 2x18 half PL-C down light or fittings code no. LHOC 33218399 | 8 | Nos |  |  |

---------------------------

TOTAL: PART-B:

----------------------------

PART-C : 	REMOVAL & RE-FIXING OF SPLIT AIR CONDITIONING MACHINES:

| I) | Removing carefully existing AC machines (Split ACs of any brand & any capacities), Keeping them safe while the work is in progress & then re-installing the machines at new locations as directed by the consultants, P/F new refrigerant pipes, charging & testing & commissioning the machines, all complete as directed, including New electric cables, New pipes for condensate water. The cost of Electric Cables, Refrigerant Pipes, Water Pipes, Gas charging shall be paid separately as below: | 4 | Nos |  |  |
| --- | --- | --- | --- | --- | --- |
| II) | Piping, Installation, Testing & Commissioning: |  |  |  |  |
| 1 | REFRIGERATION PIPING: P/F copper piping for carrying refrigerant, of appropriate/approved dia, approved gauge, with approved insulation, with nitryle rubber tube, etc. complete. | 50 | Rmt |  |  |
| 2 | ELECTRIC CABLING: P/L Electric cabling of required rated capacity as directed, from out door unit to indoor unit. | 50 | Rmt |  |  |
| 3 | PVC DRAIN PIPES: P/F PVC drain piping for draining condensate water, including all the fittings, fixtures, etc. complete. | 50 | Rmt |  |  |
| 5 | INSTALLATION, GAS CHARGING, COMMISSIONING, TESTING: Installation, gas-charging, commissioning, & Testing of Air-conditioning Machines/Units, etc., complete. | 4 | Nos. |  |  |

---------------------------------

TOTAL: PART-C:

-----------------------------------

## SUMMARY

| PART-A: INTERIOR WORKS (FURNITURE & CIVIL) | : | TOTAL Rs. |
| --- | --- | --- |
| PART-B: ELECTRICAL WORKS | : | TOTAL Rs. |
| PART-C:RE-INSTALLATION OF AIR CONDITIONING MACHINES: |  | TOTAL Rs. |
| GRAND TOTAL OF (A+B+C) | : | TOTAL Rs. |
| Less: Discount (if any) ______ % | : | (-) Rs. |
|  | : | TOTAL Rs. |
| Add: VAT: _____________ % | : | Rs. |
| Add: Serv Tax: _____________ % | : | Rs. |
| NET OFFER | : | TOTAL Rs. |

(Rupees ______________________________________________________________

____________________________________________________________________).

Contractor’s Signature with seal.

Dated:

ANNEXURE-I

(Information about the contractor. To be filled-in by the contractor)

1. Name of the Firm:

2. Office Address:

3. Tel. Nos (Off.):

Fax:

2. Factory Address:

3. Tel. Nos (Fact.):

4. Constitution of Firm		:

(Proprietary/Partnership/

Pvt. Ltd. Co./Ltd. Co.,)

5. Date of Formation		:

6. Details about Proprietor/ Managing Partner/M. Director:

- Full Name:

- Designation:                                     Age:         Yrs.,      Qualifications:

- Resi. Address	:

- Res. Tel. Nos :

- Personal Mobile No.:

7. Bankers Name & Branch.		A/C No. 			Limit of O.D./C.C.

Rs. __________________

Rs. __________________

8. Income Tax PAN No.	:

9. VAT Reg. No.		:

10. Service Tax Reg. No.:

11. Experience in the field of: Renovation/Interior works:                  Years.

***********************